## Slide 1: OL Series 750 Automated Spectroradiometric Measurement System

## Slide 2: ABOUT OPTRONIC LABORATORIES, LLC • Optronic Laboratories, LLC was established in 1970 by two eminent researchers at NIST (then NBS). Facilities were modeled after NIST, and Optronic Laboratories, LLC achieved a worldwide reputation for excellence in light measurement and calibration. • Continuing to work closely with NIST, the development of new instruments and techniques at Optronic Laboratories, LLC constantly improves the accuracy and precision of light measurement.
BACKGROUND

## Slide 3: OPTRONIC LABORATORIES’ INSTRUMENTS & SERVICES INCLUDE: • Training, consultation & advice
BACKGROUND

## Slide 4: THE HEART OF ANY SPECTRORADIOMETRIC SYSTEM IS THE MONOCHROMATOR, BUT… • It must give the right bypass – - Too large and spectra are distorted - Too small and signals are low • It must give high spectral purity (low stray light) so only the wavelength of interest is detected
THE OL SERIES 750 MONOCHROMATORS

## Slide 5: • Available in single and double (shown) versions • F/4 optics for high throughput • Very low stray light • Numerous special features for most accurate results
THE OL SERIES 750 MONOCHROMATORS

## Slide 6: • Large range of gratings available • Optimized for high efficiency • Optimized for wide wavelength range • Optimized for high resolution
THE OL SERIES 750 MONOCHROMATORS
Tri-grating mounts change gratings automatically

## Slide 7: • Range of plug-in input accessories • Choppers (shown) for IR detectors • Automatic control of chopper speed and “open” position stop • Filter-wheel for input attenuation or filtering
THE OL SERIES 750 MONOCHROMATORS
Versatile plug-in chopper or filter wheel input accessories

## Slide 8: • Fully automated 11 position blocking-filter wheel • Includes SHUT position for dark current readings • Optimized filters for widest wavelength range
THE OL SERIES 750 MONOCHROMATORS
Blocking-filter wheel changes filters automatically

## Slide 9: • Gratings diffract light at different angles depending on wavelength • 400nm will also diffract at the same angle as 800nm (since 2 x 400 = 800) • A blocking filter removes the 400nm so just 800nm is left
THE OL SERIES 750 MONOCHROMATORS
Blocking filters:
how they work
400nm + 800nm
400nm
400nm
800nm
Blocking filter
grating

## Slide 10: • Light passes into the monochromator through the entrance slit, then onto the first collimating mirror.
THE OL SERIES 750 MONOCHROMATORS

## Slide 11: • Collimated (parallel) light is directed onto the grating.
THE OL SERIES 750 MONOCHROMATORS

## Slide 12: • The grating diffracts the light, sending each wavelength off at a different angle. • The desired wavelength is collected by the first focussing mirror….
THE OL SERIES 750 MONOCHROMATORS

## Slide 13: • …which focuses it at the middle slit. • A second collimating mirror collects this beam…
THE OL SERIES 750 MONOCHROMATORS

## Slide 14: • …and collimates it onto a second grating. • Since the second grating is linked to the first, they are at the same angle and hence the same wavelength.
THE OL SERIES 750 MONOCHROMATORS

## Slide 15: • This second grating acts like the first, but the spectral purity is increased by many decades.
THE OL SERIES 750 MONOCHROMATORS

## Slide 16: • The pure monochromatic light, at the wavelength desired, is then focussed onto the exit slit and emerges from the monochromator
THE OL SERIES 750 MONOCHROMATORS

## Slide 17: • Single and double lamp versions • UV lamp - 200nm to 400nm • Tungsten lamp - 250nm to 2500nm • Glowbar - 1000nm to 30000nm
THE OL SERIES 740-20
LIGHT SOURCES

## Slide 18: • Optics match the OL Series 750 Monochromators • Easy switching from one source …
THE OL SERIES 740-20
LIGHT SOURCES

## Slide 19: • Optics match the OL Series 750 Monochromators • Easy switching from one source … …TO THE OTHER
THE OL SERIES 740-20
LIGHT SOURCES
Fully automated switching available

## Slide 20: • 200 to 30,000 nm coverage • Monochromatic light prevents sample heating • Suits a very wide range of standard OL accessories • Suits many existing and future applications
THE OL 750 + OL 740-20

## Slide 21: • In order to characterize their performance in a particular applications, single detectors, array detectors and assemblies often need spectral response to be known • For example, photopic detectors can be analysed for V() matching
DETECTOR
SPECTRAL RESPONSE

## Slide 22: • Measurements are generally consistent with detector use, and may require a large collimated beam, a small spot, a diffuse source or other geometry • Optronic Laboratories, LLC manufactures a wide range of accessories for most detector measurement requirements, including quantum efficiency
DETECTOR
SPECTRAL RESPONSE

## Slide 23: • Optronic Laboratories, LLC provides standard detectors, traceable to NIST and other National Laboratories • To illustrate a detector spectral response system, we will use the OL 750-10C All Mirror Collimator
DETECTOR
SPECTRAL RESPONSE

## Slide 24: • 1 inch diameter beam • Excellent beam uniformity • Constant collimation at all wavelengths
THE OL 750-11C

## Slide 25: • If we put these together…
THE OL 750 + OL 740-20
+ OL 750-11C

## Slide 26: • We have a complete system for detector response
THE OL 750 + OL 740-20
+ OL 750-11C
Then we measure the test detector

## Slide 27: • The system illustrated represents just a few of the accessories from Optronic Laboratories, LLC. • For more information: Visit our website at OptronicLabs.com Call 407-422-3171 to Contact an Application Engineer
MORE INFORMATION